# NeXus Instrument Definitions for Muon Data

This paper presents Revision 8 of a new Muon NeXus Instrument Definition (Version 2), with the original version included for comparison.

This revision was made following discussions with PSI, considering the prototype version 2 definition in anticipation of using the definition as a muon exchange format.

Stephen Cottrell

24 December 2011

## Table of Contents

NeXus Instrument Definitions for ISIS muon Data	1

Table of Contents	2

Muon Instrument Definition: Version 1	4

NXfile	5

NXentry	6

NXuser	7

NXlog	8

NXsample	9

NXinstrument	10

NXdetector	11

NXcollimator	12

NXbeam	13

NXdata	14

Notes:	16

Muon Instrument Definition: Version 2 – ‘pulsedTD’	19

NXroot	20

NXentry	21

NXuser	23

NXrunlog	24

NXselog	25

NXperiod	26

NXsample	27

NXenvironment	29

NXinstrument	30

NXdata	31

NXcharacterization	32

NXsensor	33

NXsource	34

NXbeamline	36

NXdiagnostics	37

NXdipole_magnet	38

NXquadrupole_magnet	39

NXseptum_magnet	40

NXsolenoid_magnet	41

NXsteering_magnet	42

NXseparator	43

NXspin_rotator	44

NXmagnetic_kicker	45

NXelectrostatic_kicker	46

NXbeamline_collimator	47

NXdae	48

NXdetector	49

NXlog	52

NXgeometry	53

NXshape	54

NXtranslation	55

NXorientation	56

Notes:	57

General comments:	60

Appendix 1: Class definitions unique to ‘muonTD’	62

Appendix 2: Incorporating SECI logged values	64

## Muon Instrument Definition: Version 1

This data format evolved as a student project with the following outcome:

- CONVERT_NEXUS written to convert MCS raw files to NeXus using this Instrument Definition.

- TMOGGER written to plot temperature and data logs with the same time axis.

- Read Routines provided in Fortran 77 and C for inclusion in user code.

- UDA and WIMDA adapted to read the data format.

- Format written automatically by MuSR and EMU on a central PC disk as an alternative file format.

- Defined in RAL Technical Report: D. Flannery, S.P. Cottrell, P.J.C. King, RAL-TR-2001-029, August 2001.

### NXfile

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXfile |  |  | Top level class |  |
|  |  | NeXus_version | NX_CHAR | Version of NeXus API used to create file |  |
|  |  | user | NX_CHAR | Scientist who performed experiment |  |
|  | run |  | NXentry |  | First (and only) entry |

### NXentry

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXentry |  |  | Name of entry |  |
|  | IDF_version |  | NX_INT32 | version of IDF that NeXus file conforms to |  |
|  | program_name |  | NX_CHAR | name of creating program – ‘MCS’ |  |
|  |  | version | NX_CHAR | version of creating program |  |
|  | number |  | NX_INT32 | run number |  |
|  | title |  | NX_CHAR | string containing sample, temperature and field |  |
|  | notes |  | NX_CHAR | comment from MCS file |  |
|  | analysis |  | NX_CHAR | type of muon experiment - “muonTD” (muon, time differential) |  |
|  | lab |  | NX_CHAR | origin of experiment – “ISIS” (collected at the ISIS facility) |  |
|  | beamline |  | NX_CHAR | particular beamline used for experiment |  |
|  | start_time |  | NX_CHAR | start time and date of measurement |  |
|  | end_time |  | NX_CHAR | stop time and date of measurement |  |
|  | duration |  | NX_CHAR | calculated duration |  |
|  | switching_states |  | NX_INT32 | ‘1’ – Normal data collection, ‘2’ – Red/Green mode |  |
|  | user |  | NXuser |  | Details of PI |
|  | sample |  | NXsample |  | Details of the sample under investigation |
|  | instrument |  | NXinstrument |  | Details of the instrument used |
|  | histogram_data_1 |  | NXdata |  | The data collected |
|  | temperature_log |  | NXlog |  | Log of temperature values during run |
|  | event_log |  | NXlog |  | Log of events captured during run |

### NXuser

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXuser |  |  | name of user |  |
|  | name |  | NX_CHAR | scientist(s) name |  |
|  | experiment_number |  | NX_CHAR | RB number |  |

### NXlog

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXlog |  |  | name of log |  |
|  | name |  | NX_CHAR | name of log | e.g. ‘sample temperature’ |
|  |  | available | NX_INT32 | number of values |  |
|  | values |  | NX_FLOAT | log of values | e.g. ‘temperature values obtained from the ‘TLOG’ file |
|  |  | units | NX_CHAR | units of values | e.g. ‘kelvin’ |
|  | time |  | NX_FLOAT | time stamp of values | from start of run |
|  |  | units | NX_CHAR | units of time stamps | e.g. ‘seconds’ |

### NXsample

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXsample |  |  | sample |  |
|  | name |  | NX_CHAR | sample name |  |
|  | temperature |  | NX_FLOAT | temperature setting | Desired temperature |
|  |  | units | NX_CHAR | units for temperature | e.g. ‘kelvin’ |
|  | magnetic_field |  | NX_FLOAT | Field setting | Desired magnetic field |
|  |  | units | NX_CHAR | units for field | e.g. ‘gauss’ |
|  | shape |  | NX_CHAR | sample orientation |  |
|  | magnetic_field_state |  | NX_CHAR | mode | e.g. ‘TF’ |
|  | magnetic_field_vector |  | NX_FLOAT[] | vector describing magnetic field orientation |  |
|  |  | coordinate_system | NX_CHAR | coordinate system | e.g. ‘cartesian’ |
|  |  | units | NX_CHAR | units for field | e.g. ‘gauss’ |
|  |  | available | NX_INT32 | available | attribute ‘1’ if field vector is available, otherwise ‘0’ |
|  | environment |  | NX_CHAR | rig | e.g.’CCR’ |
|  | temperature_log |  | NXlink | link to temperature log |  |

### NXinstrument

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXinstrument |  |  | name |  |
|  | name |  | NX_CHAR | instrument name |  |
|  | detector |  | NXdetector |  |  |
|  | collimator |  | NXcollimator |  |  |
|  | beam |  | NXbeam |  |  |

### NXdetector

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXdetector |  |  | detector name |  |
|  | number |  | NX_INT32 | number of detectors |  |
|  | orientation |  | NX_CHAR | detector arrangement, ‘Longitudinal (“l”)’ or ‘Transverse (“t”)’ |  |
|  | angles |  | NX_FLOAT32[][] | 2D array defining detector positions | (see Note 1) |
|  |  | coordinate_system | NX_CHAR | coordinate_sytem | e.g. ‘cartesian’ |
|  |  | available | NX_INT32 | available | attribute ‘1’ if angles are available, otherwise ‘0’ |
|  | deadtimes |  | NX_FLOAT32[] | 1D array of detector deadtime values | (see Note 2) |
|  |  | units | NX_CHAR | ‘microseconds’ |  |
|  |  | available | NX_INT32 | available | attribute ‘1’ if deadtimes are available, otherwise ‘0’ |

### NXcollimator

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXcollimator |  |  | collimator name |  |
|  | type |  | NX_CHAR | ‘slits’ |  |
|  | aperture |  | NX_CHAR | slit setting | not defined by MCS |

### NXbeam

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXbeam |  |  | beamline |  |
|  | event_log_1 |  | NXlink | link to event log |  |
|  | total_counts |  | NX_FLOAT32 | counts | total number of counts |
|  |  | units | NX_CHAR | ‘Mev’ |  |
|  | daereads |  | NX_INT32 | daereads | number of readouts from the DAE |
|  | frames |  | NX_INT32 | frames | ISIS frames collected on each DAE read |

### NXdata

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXdata |  |  | dataset name | (see note 3) |
|  | counts |  | NX_INT32[][] | raw data counts | 2D array of counts: (detector number * switching_states) vs. bin |
|  |  | units | NX_CHAR | ‘counts’ | required by NeXus |
|  |  | signal | NX_INT32 | ‘1’ | attribute to indicate signal to be plotted |
|  |  | number | NX_INT32 | number of histograms | attribute, number of histograms in NXdata group (see Note 4) |
|  |  | length | NX_INT32 | length of histograms | attribute, length of histograms in bins |
|  |  | t0_bin | NX_INT32 | bin for time zero | attribute, t0 bin value for histograms |
|  |  | first_good_bin | NX_INT32 | first good bin | attribute, first good bin values for histograms |
|  |  | last_good_bin | NX_INT32 | last good bin | attribute, last good bin values for histograms |
|  |  | offset | NX_FLOAT32 | offset | attribute giving offset to centre of 1st bin - 0.5*histogram_resolution |
|  | resolution |  | NX_INT32 |  | histogram resolution, set to zero if not applicable |
|  |  | units | NX_CHAR | ‘picoseconds’ | attribute to describe resolution units |
|  | time_zero |  | NX_INT32 |  | time zero for muon measurements (see Note 5) |
|  |  | units | NX_CHAR | ‘microseconds’ | attribute to describe time_zero units |
|  |  | available | NX_INT32 | available | Attribute, time zero (“0” if not available) |
|  | raw_time |  | NX_FLOAT32[] | raw time | scale for time axis (raw time) in microseconds |
|  |  | axis | NX_INT32 | ‘1’ | fastest varying index |
|  |  | primary | NX_INT32 | ‘1’ | raw time is the defaul |
|  |  | units | NX_CHAR | ‘microseconds’ | attribute to describe time units |
|  | corrected_time |  | NX_FLOAT32[] | corrected time | scale for time axis (corrected for ‘histogram_timezero’) |
|  |  | axis | NX_INT32 | ‘1’ | fastest varying index (2nd axis) |
|  |  | units | NX_CHAR | ‘microseconds’ | attribute to describe time units |
|  | grouping |  | NX_INT32[ng/2] | grouping | 1D array defining grouping for histograms in NXdata (see Note 6) |
|  |  | available | NX_INT32 | available | attribute, number of groups (“0” if information not available) |
|  | alpha |  | NX_FLOAT32[ng/2][3] | available | 2D array, alpha, for pairs of groups defined in ‘grouping’ (see Note 7) |
|  |  | available | NX_INT32 | available | attribute, number of pairs for which alpha is defined (“0” if not in use) |

## Notes:

Coordinate systems: Coordinate axes are taken with the z-axis pointing along the beam direction and the x-axis defined as vertically upwards, the origin is taken to be at the centre of the spectrometer (the sample position). Cartesian, cylindrical and spherical polar coordinate systems may be used with angles ( (rotation about the beam axis) and ( (rotation about an axis perpendicular to the beam direction) increasing for clockwise rotations viewed from the origin of the coordinate system.

Note 1: 2D array describing detector positions and solid angles. The index of the 1st rank represents the detector number and the first three elements of the 2nd rank define the position in the specified coordinate system. The fourth element of the 2nd rank defines the detector solid angle.

Note 2: The deadtime values for each detector. The values, read from the default deadtime file ‘DT(E)PAR.DAT’, are stored as a 1D array where the index represents the detector number. The attribute ‘deadtimes_available’ should be set to “1” if this information is read successfully, otherwise “0”.

Note 3: MCS can generate datasets where individual histograms can have different resolutions, lengths, t0 bins, first good bins and last good bins! In practice this feature is rarely used. For efficiency, the muon NeXus instrument definition specifies that sets of histograms where these five parameters are common are grouped into a single NXdata group. Most ISIS muon NeXus files will therefore contain a single NXdata group.

Note 4: The value of the attribute ‘histogram_number’ should be set equal to the total number of histograms in the NXdata group. The value should reflect any histogram doubling resulting from the Red/Green data collection mode.

Note 5: Not defined in the MCS file, the value should be read from the file ‘BASETIME.UDA’ if this is available in the current directory. The attribute ‘available’ should be set accordingly.

Note 6: If there is a grouping file (‘long.uda’ for longitudinal data and ‘trans.uda’ for transverse data) in the directory where the NeXus file is being created then this should be used. If this is not available, the default grouping file corresponding to the current instrument orientation should be used. A check should be made that the total number of histograms listed in the grouping file corresponds to the value of ‘histogram_number’ in the NeXus file, with a mismatch indicating an error. The attribute ‘grouping_available’ should be set equal to the total number of groups unless grouping information is not available or there is an error condition, when it should be set to “0”. The grouping is represented as a 1D array with the index representing the histogram number and the value corresponding to the group into which it should be placed.

Note 7: The balance parameter, alpha, is given for pairs of groups defined in ‘grouping’. Values are stored in a 2D array together with the numbers for the forward and backward groups. The attribute ‘alpha_available’ should be set to the number of alpha values defined or zero if not in use.

Note 8: NXLOG groups can be added as required for any variables logged during an experiment. Logged groups should contain a values array and units and a corresponding time array and units.

## Muon Instrument Definition: Version 2 – ‘pulsedTD’

A revision of the Instrument Definition is proposed for the following reasons:

- To correct misunderstandings and misinterpretations of the NeXus format before the definition moves into wider use (PSI are considering adopting NeXus as their RAW file format, and NeXus is a candidate for an exchange file format for sharing muon data between facilities).

- To bring the muon definition closer to that proposed for the neutron instruments at ISIS, from which many of the ideas in this document are taken.

- Where possible, to incorporate ideas and standards set by the NeXus International Advisory Committee (NIAC) (see http://www.nexusformat.org/Main_Page for current discussion). The new definition, however, still requires class definitions not currently defined and/or ratified by the NIAC; these are listed in Appendix 1 in preparation for ratification where applicable.

- To provide a RAW file format suitable for storing data written by PC DAE2 and that, in particular, provides the facility for handling unlimited periods in an efficient fashion.

- To provide a definition that is better able to adapt to the wide range of specialist experiments that now run at RAL. The new definition has not attempted to define all entries required for all possible experiments (e.g. RF, laser, etc), it is anticipated that the basic definition (together with the necessary ‘read’ routines) will be extended to accommodate the additional information as required. Guidelines are provided to assist the extension of the basic definition in a compatible way.

The Instrument Definition described in this document is uniquely identified by the data entries ‘idf_version’ (‘2’) and ‘definition’ (‘pulsedTD’) stored within the ‘NXentry’ group, and the attribute ‘creator’ (‘ISIS’) in the group ‘NXroot’. It is specifically designed for the ISIS muon instruments (EC and RIKEN-RAL) for storing raw data files, although it should be equally applicable to other pulsed muon sources (with appropriate localisation). For continuous sources, modifications appear inevitable; however, it is hoped that the majority of the meta-data can be written in a compatible fashion. It is vital for reading programs that any modification to entries in the existing definition should be marked by new values written for the ‘definition’, ‘version’ and ‘creator’ entries. A simple extension of the definition need not yield a new version number, although reading programs would then need to use other methods to discover the additional data. The NXuif group provides a convenient area to store user/experiment specific information.

### NXroot

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXroot |  |  |  | top level class |
| 1 |  | file_name | NX_CHAR |  | file name of original data file to assist identification if the external name has been changed |
| 1 |  | file_time | ISO 8601 |  | date and time of file creation |
| 0/1 |  | Initial_file_format | NX_CHAR | ‘HDF(4)’ ¦ ‘HDF(5)’ ¦ ‘XML’ | Format used when creating initial NeXus file |
| 0/1 |  | file_update_time | ISO 8601 |  | date and time of last file update at close |
| 0/1 |  | NeXus_version | NX_CHAR |  | version of nexus API used in writing the file |
| 0/1 |  | HDF_version | NX_CHAR |  | version of HDF library used by nexus to create file |
| 0/1 |  | HDF5_version | NX_CHAR |  | version of HDF5 library used by nexus to create file |
| 0/1 |  | XML_version | NX_CHAR |  | version of XML library used to create file |
| 1 |  | creator | NX_CHAR |  | facility or program where file originated |
| 1+ | {raw_data_*} |  | NXentry |  | Entries holding the raw data should follow the defined naming convention and be numbered; entries may also be written containing analysed data etc using a locally defined naming scheme. |

### NXentry

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXentry |  |  |  | name of entry |
| 1 | idf_version |  | NX_INT | ‘2’ | version of IDF that NeXus file confirms to |
| 1 | definition |  | NX_CHAR | ‘muonTD’ | the template (DTD name) on which the entry was based, e.g. ‘muonTD’ (muon, time differential). It’s suggested that muon definitions always use the prefix ‘muon’, with a subsequent sequence of capitals defining the unique function of the definition. |
| 0/1 |  | version | NX_CHAR |  | DTD version number |
| 0/1 |  | URL | NX_CHAR |  | URL of XML DTD or schema appropriate for file |
| 0/1 | definition_local |  | NX_CHAR |  | a template (DTD name) on which an extension to the base definition is based |
| 0/1 |  | version | NX_CHAR |  | DTD version number |
| 0/1 |  | URL | NX_CHAR |  | URL of XML DTD or schema appropriate for file |
| 0/1 | program_name |  | NX_CHAR | ‘SECI’ ¦ ‘MCS’ ¦ ‘CONVERT_NEXUS’ | name of creating program |
| 0/1 |  | version | NX_CHAR |  | version of creating program |
| 0/1 |  | configuration | NX_CHAR |  | configuration of software e.g. SECI configuration |
| 1 | run_number |  | NX_INT |  | run number |
| 1 | title |  | NX_CHAR |  | extended title for the entry, e.g. string containing sample, temperature and field |
| 0/1 | notes |  | NX_CHAR |  | log of useful stuff about the experiment, supplied by the user |
| 1 | start_time |  | ISO 8601 |  | start time and date of measurement |
| 1 | end_time |  | ISO 8601 |  | end time and date of measurement |
| 0/1 | duration |  | NX_INT |  | duration of measurement i.e. (end-start) |
| 0/1 |  | units | NX_CHAR | ‘second’ |  |
| 0/1 | collection_time |  | NX_FLOAT |  | duration of data collection, taking out periods when collection was suspended (e.g. because of a beam off or run control veto) |
| 0/1 |  | units | NX_CHAR | ‘second’ |  |
| 0/1 | total_counts |  | NX_INT |  | total number of detector events |
| 0/1 | good_frames |  | NX_INT |  | number of proton pulses used (not vetoed) |
| 0/1 | raw_frames |  | NX_INT |  | number of proton pulses to target |
| 0/1 | proton_charge |  | NX_FLOAT |  |  |
| 0/1 |  | units | NX_CHAR | microAmp*hour |  |
| 1 | experiment_identifier |  | NX_CHAR |  | experiment number, for ISIS, the RB number |
| 0/1 | run_cycle |  | NX_CHAR |  | ISIS cycle |
| 1 | user_1 |  | NXuser |  | details of representative user |
| 0/1+ | {experiment team} |  | NXuser |  | details of members of experiment team, numbered in sequence |
| 0/1 | runlog |  | NXrunlog |  | container for log(s) of run parameters, inevitably specific to each facility. See Note 0 |
| 0/1 | selog |  | NXselog |  | container for log(s) of sample environment parameters, that may be specific to each experiment. |
| 0/1 | periods |  | NXperiod |  | log of period parameters, inevitably specific to each facility. See Note 0 |
| 1 | sample |  | NXsample |  | details of the sample under investigation |
| 1 | instrument |  | NXinstrument |  | details of the instrument used |
| 1+ | {detector_*} |  | NXdata |  | the data collected (see Note 1) |
| 0/1+ | {characterization} |  | NXcharacterization |  | contains a link calibration data, e.g. silver runs, spot size measurements. |
| 0/1 | uif |  | NXuif |  | group containing user supplied information contents of group not defined in definition |

### NXuser

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXuser |  |  |  | name of user |
| 1 | name |  | NX_CHAR |  | full name of user |
| 0/1 |  | role | NX_CHAR |  | role of user e.g. ‘PI’, ‘Contact’ etc, multiple roles are allowed. |
| 0/1 | affiliation |  | NX_CHAR |  | institute |
| 0/1 | address |  | NX_CHAR |  | address |
| 0/1 | telephone_number |  | NX_CHAR |  | telephone number |
| 0/1 | fax_number |  | NX_CHAR |  | FAX |
| 0/1 | email |  | NX_CHAR |  | email |
| 0/1 | facility_user_id |  | NX_CHAR |  | unique facility based identifier, at ISIS the User Number |

### NXrunlog

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXrunlog |  |  |  |  |
| Class to contain action and acquisition logs arising from activities of the data acquisition electronics (DAE) during the run – entries will be facility specific. |

### NXselog

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXselog |  |  |  |  |
| Class to contain sample environment logs arising from activities of the experiment control software – entries will be facility specific. |

### NXperiod

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXperiod |  |  |  |  |
| 1 | number |  | NX_INT | ‘np’ | number of periods used |
| 1 | type |  | NX_INT[np] | ‘1’ ¦ ‘2’ | function of period: ‘1’ – DAQ, ‘2’ – DWELL |
| 1 | frames_requested |  | NX_INT[np] |  | frames collected in each period before switching, ‘0’ for unlimited frames |
| 1 |  | frame_type | NX_CHAR | ‘good’ ¦ ‘raw’ | type of frame for period switching |
| 0/1 | output |  | NX_INT[np] |  | output bit pattern on period card. If not known, write ‘0’ … ‘np’-1 into array |
| 0/1 | labels |  | NX_CHAR |  | list of period names, separated by character given as attribute. May use a 2D array of NX_CHAR - TBC |
| 0/1 |  | separator | NX_CHAR |  | separator character for label list |
| 0/1 | raw_frames |  | NX_INT[np] |  | raw frames collected for each period |
| 0/1 | good_frames |  | NX_INT[np] |  | good frames collected for each period |
| 0/1 | sequences |  | NX_INT[np] |  | number of times data collection took place in each period |
| 0/1 | counts |  | NXlog |  | counts collected in each periods |
| Additional entries may be stored to clarify Period activity. |

### NXsample

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXsample |  |  |  | sample |
| 1 | name |  | NX_CHAR |  | sample name |
| 0/1 | chemical_formula |  | NX_CHAR |  | element symbols to be arranged in ‘Hill System’ order: C, H, then other elements alphabetically |
| 0/1 | description |  | NX_CHAR |  | description of sample |
| 0/1 | type |  | NX_CHAR | ‘sample’ ¦ ‘calibration sample’ ¦ ‘normalisation sample’ ¦ ‘simulated data’ ¦ ‘none’ ¦ ‘sample environment’ | type of sample |
| 0/1 | situation |  | NX_CHAR | ‘atmosphere’ ¦ ‘vacuum’ |  |
| 0/1 | preparation_date |  | ISO 8601 |  | date of preparation of sample |
| 0/1 | sample_holder |  | NX_CHAR |  | description of sample holder |
| 0/1 | flypast |  | NX_INT | ‘0’ ¦ ‘1’ | flypast (suspended sample) mounting: ‘0’ – No, ‘1’ – Yes |
| 0/1 | geometry |  | NXgeometry |  | sample size |
| 0/1 | sample_component |  | NX_CHAR[n_comp] |  | name of each sample componenet |
| 0/1 | thickness |  | NX_FLOAT[n_comp] |  | sample thickness, may be multiple components |
| 0/1 |  | units | NX_CHAR | ‘milli.metre’ |  |
| 0/1 | mass |  | NX_FLOAT[n_comp] |  | sample mass, may be multiple components |
| 0/1 |  | units | NX_CHAR | ‘milli.gram’ |  |
| 0/1 | density |  | NX_FLOAT[n_comp] |  | sample density, may be multiple components |
| 0/1 |  | units | NX_CHAR | ‘milli.gram.centimetre-3’ |  |
| 0/1 | temperature |  | NX_FLOAT |  | linked to most representative sample temperature (to help cataloguing programs) |
| 0/1 | magnetic_field |  | NX_FLOAT[] |  | linked to most representative magnetic field (to help cataloguing programs) |
| 0/1 | magnetic_field_state |  | NX_CHAR | ‘LF’ ¦ ‘TF’ ¦ ‘ZF’ | current field operating mode |
| 0/1+ | temperature_* |  | NX_FLOAT |  | temperature (see Note 2) |
| 0/1+ |  | units | NX_CHAR | ‘kelvin’ | units for temperature |
| 0/1+ |  | role | NX_CHAR | ‘control’ ¦ ‘sample’ | function of temperature |
| 0/1+ |  | value | NX_CHAR | ‘nominal’ ¦ ‘derived’ | .eq. |
| 0/1+ | temperature_*_env |  | NXenvironment |  | details of associated hardware |
| 0/1+ | temperature_*_log |  | NXlog |  | temperature log |
| 0/1+ | magnetic_field_* |  | NX_FLOAT[] | field setting | magnetic field, may be a vector |
| 0/1+ |  | units | NX_CHAR | ‘gauss’ | units for field |
| 0/1+ |  | role | NX_CHAR | ‘active’ ¦ ‘inactive’ | field status |
| 0/1+ |  | direction | NX_CHAR | ‘x’ ¦ ‘y’ ¦ ‘z’ | field direction |
| 0/1+ | magnetic_field_*_env |  | NXenvironment |  | details of associated hardware |
| 0/1+ | magnetic_field_*_log |  | NXlog |  | log of field values – extension to NeXus to enable log of vector quantities |

### NXenvironment

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXenvironment |  |  |  |  |
| 1 | name |  | NX_CHAR |  | name of apparatus |
| 0/1 | short_name |  | NX_CHAR |  | name displayed on DAE software |
| 0/1 | type |  | NX_CHAR |  | short code |
| 0/1 | description |  | NX_CHAR |  | long description |
| 0/1 | program |  | NX_CHAR |  | version of driver used to collect data, e.g. VI name and version |
| 0/1+ | {hardware log} |  | NXlog |  | log of hardware parameter relating to apparatus, e.g. temperature controller parameters, etc |
| 0/1+ | {sensor name} |  | NXsensor |  |  |

### NXinstrument

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXinstrument |  |  |  | name |
| 1 | name |  | NX_CHAR |  | instrument name |
| 1 | source |  | NXsource |  | details of the muon source used |
| 1 | beamline |  | NXbeamline |  | beamline description |
| 1+ | {detector_*} |  | NXdetector |  | details of detector used |
| 0/1 | dae |  | NXdae |  | Details of the DAE used. See note 0. |
| 0/1+ | {aperture} |  | NXlink |  | link to aperture in NXbeamline (naming must be identical) apertures used to collimate beam (only link those that the user is interested in) |

### NXdata

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXdata |  |  |  |  |
| 1 | counts |  | NX_INT[ns] ¦ NX_INT[ns][ntc] ¦ NX_INT[np][ns][ntc] |  | linked to detector counts in NXdetector |
| 1 |  | signal | NX_INT | ‘1’ |  |
| 1 |  | axes | NX_CHAR | ‘[period_index, spectrum_index, raw_time]’ | axes definitions |
| 1 |  | long_name | NX_CHAR | ‘positron counts’ ¦ ‘electron counts’ |  |
| 0/1 | raw_time |  | NX_FLOAT[ntc+1] |  | linked to ‘raw_time’ in NXdetector |
| 0/1 |  | units | NX_CHAR | ‘micro.second’ |  |
| 0/1 |  | long_name | NX_CHAR | ‘time’ |  |
| 0/1 | spectrum_index |  | NX_INT[ns] |  | linked to ‘spectrum_index’ in NXdetector (see Note 3) |
| 0/1 |  | long_name | NX_CHAR | ‘spectrum number’ |  |
| 0/1 | spectrum_labels |  | NX_CHAR |  | linked to semicolon separated list of spectrum names |
| 0/1 | period_index |  | NX_INT[np] |  | link to ‘period_index’ in NXdetector |
| 0/1 |  | long_name | NX_CHAR | ‘period number’ |  |
| 0/1 | period_output |  | NX_INT[np] |  | linked to ‘period_output’ in NXperiod - usually integer representing output bit pattern on period card |
| 0/1 | period_labels |  | NX_CHAR |  | linked to semicolon separated list of period names |

### NXcharacterization

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXcharacterization |  |  | {type of characterization} | name of group should reflect type of characterization |
| 0/1 | source |  | NX_CHAR |  | source file, if missing then use current file |
| 1 | location |  | NX_CHAR |  | path to data in file |
| 0/1 | mime_type |  | NX_CHAR |  | if missing, the source file is NAPI readablee |
| 0/1 | definition |  | NX_CHAR |  | definition data conforms to |
| 0/1 |  | version | NX_CHAR |  | version of definition |

### NXsensor

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXsensor |  |  |  |  |
| 0/1 | model |  | NX_CHAR |  | sensor model number, e.g. ‘RhFe 11074’ |
| 1 | name |  | NX_CHAR |  | name |
| 0/1 | short_name |  | NX_CHAR |  | name displayed on DAE software, e.g. SECI block name |
| 0/1 | attached_to |  | NX_CHAR |  | where sensor is attached |
| 0/1 | measurement |  | NX_CHAR | ‘temperature ¦ pH ¦ magnetic_field ¦ electric field ¦ conductivity ¦ resistance ¦ voltage ¦ pressure ¦ flow ¦ stress ¦ strain ¦ shear ¦ surface_pressure’ | type of measurement |
| 0/1 | type |  | NX_CHAR | e.g. ‘Rh/Fe ¦ Cernox ¦ Hall ¦ NMR’ | type of probe making the measurement |
| 0/1 | run_control |  | NX_BOOLEAN |  | is data collection controlled by sensor value |
| 0/1 | high_trip_value |  | NX_FLOAT |  | if using run control, upper bound |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | low_trip_value |  | NX_FLOAT |  | if using run control, lower bound |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | value |  | NX_FLOAT[] |  | sensor value |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | value_log |  | NXlog |  | log of sensor value |

### NXsource

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXsource |  |  |  | name of source |
| 1 | name |  | NX_CHAR |  | facility name |
| 1 | type |  | NX_CHAR | ‘pulsed muon source’ ¦ ‘low energy muon source’ |  |
| 1 | probe |  | NX_CHAR | ‘positive muons’ ¦ ‘negative muons’ |  |
| 0/1 | source_frequency |  | NX_FLOAT |  | accelerator frequency, note that some frames may be ‘missing’ at target |
| 0/1 |  | units | NX_CHAR | ‘hertz’ |  |
| 0/1 | source_frequency_log |  | NXlog |  | log of source frequency during run |
| 0/1 | source_frame_pattern |  | NX_INT[rep_len] |  | frame pattern: ‘1’ frame to target, ‘0’ frame missing at ‘frequency’, e.g. ISIS target 1 with TS2: ‘1,1,1,1,0’, with a ‘rep_len’ of ‘5’ and ‘period’ 100ms. |
| 0/1 |  | rep_len | NX_INT |  | repetition length of frame pattern in terms of frames to target |
| 0/1 |  | period | NX_FLOAT |  | period of repetition of frame pattern, e.g. 100ms at ISIS target 1, with TS2 |
| 0/1 |  | units | NX_CHAR | ‘milli.second’ | units of period |
| 0/1 |  | pulses_per_frame | NX_FLOAT |  | number of pulses for each accelerator frame, e.g. ‘2’ at ISIS |
| 0/1 | source_energy |  | NX_FLOAT |  | source energy at target |
| 0/1 |  | units | NX_CHAR | ‘mega.electronvolt’ |  |
| 0/1 | source_current |  | NX_FLOAT ¦ NXlog |  | source current - this could be an average source current for the run, or logged values |
| 0/1 |  | units | NX_CHAR | ‘micro.amp’ |  |
| 0/1 | source_current_log |  | NXlog |  | log of source current during run |
| 0/1 | source_pulse_width |  | NX_FLOAT |  | source pulse width |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | target_material |  | NX_CHAR |  | e.g. ‘carbon’ |
| 0/1 | target_thickness |  | NX_FLOAT |  | thickness of target |
| 0/1 |  | units | NX_CHAR | ‘milli.metre’ |  |
| 0/1 | pion_momentum |  | NX_FLOAT |  | pion momentum |
| 0/1 |  | units | NX_CHAR | ‘mega.electronvolt.c^-1’ |  |
| 0/1 | muon_energy |  | NX_FLOAT |  | muon energy |
| 0/1 |  | units | NX_CHAR | ‘electronvolt’ |  |
| 0/1 | muon_momentum |  | NX_FLOAT |  | muon momentum |
| 0/1 |  | units | NX_CHAR | ‘mega.electronvolt.c^-1’ |  |
| 0/1 | muon_pulse_pattern |  | NX_FLOAT[rep_len] |  | pulse pattern – ‘n’ number of pulses to instrument each frame, e.g. ISIS target 1 with TS2: ‘2,2,2,2,0’, with a ‘rep_len’ of ‘5’ and ‘period’ 100ms, assuming no muon kicker. |
| 0/1 |  | rep_len | NX_INT |  | repetition length of pulse pattern in terms of frames to target |
| 0/1 |  | period | NX_FLOAT |  | period of repetition of pulse pattern, e.g. 100ms at ISIS target 1, with TS2 |
| 0/1 |  | units | NX_CHAR | ‘milli.second’ | units of period |
| 0/1 | muon_pulse_width |  | NX_FLOAT[] |  | pulse width for each pulse in frame, e.g. 80ns at ISIS |
| 0/1 |  | units | NX_CHAR | ‘nano.second’ |  |
| 0/1 | muon_pulse_separation |  | NX_FLOAT[] |  | separation of consecutive pulses in frame, e.g. 300ns at ISIS |
| 0/1 |  | units | NX_CHAR | ‘nano.second’ |  |
| 0/1 | notes |  | NX_CHAR |  | source related messages or announcements, e.g. MCR messages |

### NXbeamline

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXbeamline |  |  |  |  |
| 1 | beamline |  | NX_CHAR |  | name |
| 0/1+ | diagnostics |  | NXdiagnostics |  | container for any beamline diagnostic information. |
| 0/1+ | {beamline component} |  | NXdipole_magnet ¦ NXquadrupole_magnet ¦ NXsolenoid_magnet ¦ NXkicker ¦ NXseparator ¦ NXspinrotator ¦ NXbeamline_collimator ¦ NXseptum_magnet ¦ NXsteering_magnet |  | beamline components |

### NXdiagnostics

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXdiagnostics |  |  |  | diagnostics |
| 1+ | type |  | NX_CHAR |  | type of diagnostic |
| Class to contain entries describing diagnostic information relating to the beamline. Pictures, etc, may be included within NXnote’s, while logged entries should use NXlog. |

### NXdipole_magnet

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXdipole_magnet |  |  |  | component name |
| 1 | description |  | NX_CHAR |  | name |
| 0/1 | source_distance |  | NX_FLOAT |  | flight path from production target |
| 0/1 |  | units | NX_CHAR | ‘metres’ |  |
| 0/1 | set_current |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_current |  | NXlog |  |  |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_voltage |  | NXlog |  |  |
| 0/1 |  | units | NX_CHAR |  |  |

### NXquadrupole_magnet

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXquadrupole_magnet |  |  |  | component name |
| 1 | description |  | NX_CHAR |  | name |
| 0/1 | source_distance |  | NX_FLOAT |  | flight path from production target |
| 0/1 |  | units | NX_CHAR | ‘metres’ |  |
| 0/1 | set_current |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_current |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_voltage |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |

### NXseptum_magnet

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXseptum_magnet |  |  |  | component name |
| 1 | description |  | NX_CHAR |  | name |
| 0/1 | source_distance |  | NX_FLOAT |  | flight path from production target |
| 0/1 |  | units | NX_CHAR | ‘metres’ |  |
| 0/1 | set_current |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_current |  | NXlog |  | value read from PS (may be logged) |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_voltage |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |

### NXsolenoid_magnet

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXsolenoid_magnet |  |  |  | component name |
| 1 | description |  | NX_CHAR |  | name |
| 0/1 | source_distance |  | NX_FLOAT |  | distance of flight path from production target |
| 0/1 |  | units | NX_CHAR | ‘metres’ |  |
| 0/1 | set_current |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_current |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_voltage |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |

### NXsteering_magnet

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXsteering_magnet |  |  |  | component name |
| 1 | description |  | NX_CHAR |  | name |
| 0/1 | source_distance |  | NX_FLOAT |  | distance of flight path from production target |
| 0/1 |  | units | NX_CHAR | ‘metres’ |  |
| 0/1 | set_current |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_current |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_voltage |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |

### NXseparator

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXseparator |  |  |  | component name |
| 1 | description |  | NX_CHAR |  | name |
| 0/1 | source_distance |  | NX_FLOAT |  | distance of flight path from production target |
| 0/1 |  | units | NX_CHAR | ‘metres’ |  |
| 0/1 | set_Bfeild_current |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_Bfield_current |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_Bfield_voltage |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | set_Efield_voltage |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_Efield_current |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_Efield_voltage |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |

### NXspin_rotator

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXspin_rotator |  |  |  | component name |
| 1 | description |  | NX_CHAR |  | name |
| 0/1 | source_distance |  | NX_FLOAT |  | distance of flight path from production target |
| 0/1 |  | units | NX_CHAR | ‘metres’ |  |
| 0/1 | set_Bfield_current |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_Bfield_current |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_Bfield_voltage |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | set_Efield_voltage |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_Efield_current |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_Efield_voltage |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |

### NXmagnetic_kicker

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXmagnetic_kicker |  |  |  | component name |
| 1 | description |  | NX_CHAR |  | name |
| 0/1 | source_distance |  | NX_FLOAT |  | distance of flight path from production target |
| 0/1 |  | units | NX_CHAR | ‘metres’ |  |
| 0/1 | timing |  | NX_FLOAT |  | kicker timing, as defined by ‘description’ attribute |
| 0/1 |  | units | NX_CHAR | ‘nano.second’ |  |
| 0/1 |  | description | NX_CHAR |  |  |
| 0/1 | set_voltage |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_voltage |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | set_current |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_currente |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |

### NXelectrostatic_kicker

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXelectrostatic_kicker |  |  |  | component name |
| 1 | description |  | NX_CHAR |  | name |
| 0/1 | source_distance |  | NX_FLOAT |  | distance of flight path from production target |
| 0/1 |  | units | NX_CHAR | ‘metres’ |  |
| 0/1 | timing |  | NX_FLOAT |  | kicker timing, as defined by ‘description’ attribute |
| 0/1 |  | units | NX_CHAR | ‘nano.second’ |  |
| 0/1 |  | description | NX_CHAR |  |  |
| 0/1 | set_voltage |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_voltage |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | set_current |  | NX_FLOAT |  | set value on PS |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | read_currente |  | NXlog |  | read from PS |
| 0/1 |  | units | NX_CHAR |  |  |

### NXbeamline_collimator

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXbeamline_collimator |  |  |  |  |
| 1 | description |  | NX_CHAR |  | name |
| 0/1 | source_distance |  | NX_FLOAT |  | distance of flight path from production target |
| 0/1 |  | units | NX_CHAR | ‘metres’ |  |
| 0/1 | shape |  | NXgeometry |  | shape of aperture |
| 0/1 | material |  | NX_CHAR |  | material from which aperture is fabricated |

### NXdae

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXdae |  |  |  |  |
| 1 | type |  | NX_CHAR | ‘ISIS_MCS’ ¦ ‘ISIS_DAE2’ ¦ ‘RIKEN-RAL_MACS-EXP’ | description of DAE hardware: form name as ‘facility’_’dae’ |
| 0/1 | interface |  | NX_CHAR | ‘CAMAC’ ¦ ‘VME’ |  |
| Class to contain entries describing the data acquisition electronics (DAE). ‘type’ is required, other entries will be facility specific. |

### NXdetector

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXdetector |  |  | detector name |  |
| 1 | description |  | NX_CHAR |  | description |
| 0/1 | orientation |  | NX_CHAR | ‘Longitudinal’ ¦ ‘Transverse’ ¦ ‘L’ ¦ ‘T’ | general detector arrangement -:legacy entry for MuSR spectrometer at ISIS |
| 1 | counts |  | NX_INT[ns] ¦ NX_INT[ns][ntc] ¦ NX_INT[np][ns][ntc] |  | 1, 2 or 3D array of counts, [period, spectrum, time bin] |
| 1 |  | signal | NX_INT | ‘1’ |  |
| 1 |  | axes | NX_CHAR | ‘[period_index, spectrum_index, raw_time]’ | axes definitions |
| 1 |  | long_name | NX_CHAR | ‘positron counts’ ¦ ‘electron counts’ |  |
| 0/1 | raw_time |  | NX_FLOAT[ntc+1] |  | linked to ‘raw_time’ in NXdetector |
| 0/1 |  | units | NX_CHAR | ‘micro.second’ |  |
| 0/1 |  | long_name | NX_CHAR | ‘time’ |  |
| 0/1 | resolution |  | NX_FLOAT |  | histogram resolution in this NXdata group, time differential data must have one of ‘histogram_resolution’ or ‘raw_time’ |
| 0/1 |  | units | NX_CHAR | ‘nano.second’ |  |
| 1 | spectrum_index |  | NX_INT[ns] |  | list of global spectra |
| 0/1 |  | long_name | NX_CHAR | ‘spectrum number’ |  |
| 0/1 | spectrum_labels |  | NX_CHAR |  | list of labels for spectra, separated by character given as attribute. May use a 2D array of NX_CHAR - TBC |
| 0/1 |  | separator | NX_CHAR |  | separator character for label list |
| 0/1 | period_index |  | NX_INT[np] |  | list of period numbers |
| 0/1 |  | long_name | NX_CHAR | ‘period index’ |  |
| 0/1 | period_labels |  | NX_CHAR |  | linked to ‘period_lables’ in NXperiod |
| 0/1 | detector_index |  | NX_INT[ns] |  | ‘dectector_index[j]’ is the location of first detector in ‘spectrum_index[j]’ in the array ‘detector_list’ (see Note 3) |
| 0/1 | detector_count |  | NX_INT[ns] |  | ‘detector_count[j]’ is the total number of detectors forming spectrum in ‘spectrum_index[j]’ (see Note 3) |
| 0/1 | detector_list |  | NX_INT[nd] |  | sorted list of detector numbers (see Note 3) |
| 0/1 | crate |  | NX_INT[nd] |  | crate number (DAE2 ISIS parameter) |
| 0/1 | slot |  | NX_INT[nd] |  | slot number (DAE2 ISIS parameter) |
| 0/1 | input |  | NX_INT[nd] |  | input number (DAE2 ISIS parameter) |
| 0/1 | type |  | NX_CHAR[nd] | ‘scintillator’ | type of detector |
| 0/1 | voltage |  | NX_FLOAT[nd] |  | PMT voltage |
| 0/1 |  | units | NX_CHAR | ‘volt’ |  |
| 0/1 | discriminator |  | NX_CHAR[nd] | ‘LE’ ¦ ‘CF’ | type of discriminator |
| 0/1 |  | name | NX_CHAR[nd] |  | Name of discriminator |
| 0/1 | threshold |  | NX_FLOAT32[nd] |  | thresholds |
| 0/1 |  | units | NX_CHAR | ‘milli.volt’ |  |
| 0/1 | output_width |  | NX_FLOAT[nd] |  | pulse widths |
| 0/1 |  | units | NX_CHAR | ‘nano.second’ |  |
| 0/1 | geometry |  | NXgeometry |  | defining detector positions (see Note 4) |
| 0/1 | solid_angle |  | NX_FLOAT[nd] |  | solid angle subtended by the detector at the sample |
| 0/1 |  | units | NX_CHAR | ‘steradian’ |  |
| 0/1 | calibrated_angles |  | NX_FLOAT[nd] |  | calibrated detector angles |
| 0/1 |  | units | NX_CHAR | ‘degree’ |  |
| 0/1 |  | calibration_date | ISO8601 |  | date when angles were determined |
| 0/1 |  | calibration_run | NX_CHAR |  | run used to determine angles |
| 0/1 | dead_time ¦ dead_time_coefficients |  | NX_FLOAT[np][nd] ¦ NX_FLOAT[np][nd][nc] |  | array of detector deadtime values (see Note 5) |
| 0/1 |  | units | NX_CHAR | ‘micro.second’ |  |
| 0/1 |  | calibration_date | ISO8601 |  | date when deadtime file was determined |
| 0/1 |  | calibration_run | NX_CHAR |  | run used to generate deadtime data |
| 0/1+ | grouping_* |  | NX_INT[np][ns] |  | preferred spectrum grouping - 1D array (see Note 6) |
| 0/1 |  | primary | NX_INT |  | define preferred grouping, if multiple entries |
| 0/1+ |  | number_groups | NX_INT | ‘ng’ | number of groups |
| 0/1+ |  | name_groups | NX_CHAR |  | semicolon separated list of group names May use a 2D array of NX_CHAR - TBC |
| 0/1+ | alpha_* |  | NX_FLOAT[ng/2][3] |  | alpha, for pairs of groups defined in ‘grouping’ - 2D array (see Note 7) |
| 0/1+ |  | number_alpha | NX_INT |  | number of alpha values defined |
| 0/1 | time_zero |  | NX_FLOAT ¦ NX_FLOAT[np][ns] |  | zero time for histograms - reference ‘raw_time’, may be global or individual to detectors |
| 0/1 |  | units | NX_CHAR | ‘micro.second’ |  |
| 0/1 | time_zero_bin |  | NX_INT ¦ NX_INT[np][ns] |  | bin equating to zero time, may be global or individual to detectors |
| 0/1 | first_good_time |  | NX_FLOAT ¦ NX_FLOAT[np][ns] |  | time for first good data - reference ‘raw_time’, may be global or individual to detectors |
| 0/1 |  | units | NX_CHAR | ‘micro.second’ |  |
| 0/1 | first_good_bin |  | NX_INT ¦ NX_INT[np][ns] |  | bin containing first good data, may be global or individual to detectors |
| 0/1 | last_good_time |  | NX_FLOAT ¦ NX_FLOAT[np][ns] |  | time for last good data - reference ‘raw_time’, may be global or individual to detectors |
| 0/1 |  | units | NX_CHAR | ‘micro.second’ |  |
| 0/1 | last_good_bin |  | NX_INT ¦ NX_INT[np][ns] |  | bin containing last good data, may be global or individual to detectors |

### NXlog

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXlog |  |  |  | name of log |
| 0/1 | description |  | NX_CHAR |  | description of log |
| 0/1 | displayname |  | NX_CHAR |  | name displayed on DAE software, e.g. SECI block name |
| 0/1 | hardware |  | NX_CHAR |  | Rig, e.g. ‘CCR’ |
| 0/1 | software |  | NX_CHAR |  | version of driver used to collect data - typically VI name and version |
| 0/1 | raw_value |  | NX_FLOAT ¦ NX_INT |  | log of raw values, e.g. voltage, etc |
| 0/1 |  | units |  |  |  |
| 1 | value |  | NX_FLOAT[] ¦ NX_INT[] ¦ NX_FLOAT[][] ¦ NX_INT[][] |  | log of values or arrays, e.g. ‘temperature values obtained from the ‘TLOG’ file |
| 1 |  | units | NX_CHAR |  |  |
| 0/1 | time |  | NX_FLOAT[] |  | time stamp of values as offsets from start time |
| 0/1 |  | start | ISO 8601 |  | time of run start |
| 0/1 |  | units | NX_CHAR |  | units of logged values |
| 0/1 | average_value |  | NX_FLOAT |  | average of logged values |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | average_value_error |  | NX_FLOAT |  | standard deviation of logged values |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | minimum_value |  | NX_FLOAT |  | minimum of logged values |
| 0/1 |  | units | NX_CHAR |  |  |
| 0/1 | maximum_value |  | NX_FLOAT |  | maximum of logged values |
| 0/1 |  | units | NX_CHAR |  |  |

### NXgeometry

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXgeometry |  |  |  | name of component |
| 0/1 | {shape} |  | NXshape |  | shape/size information of component |
| 0/1 | {translation} |  | NXtranslation |  | translation of component |
| 0/1 | {orientation} |  | NXorientation |  | orientation of componenet |
| 0/1 | description |  | NX_CHAR |  | description |
| 0/1 | component_index |  | NX_INT |  | position of the component along the beam path - sample is at 0, components upstream have negative index, components downstream have positive index |

### NXshape

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXshape |  |  |  |  |
| 0/1 | shape |  | NX_CHAR |  | defining shape |
| 0/1 | size |  | NX_FLOAT[numobj,nshapepar] |  | extent of object along local axes – defined by ‘nshapepar’ parameters |
| 0/1 |  | units | NX_CHAR |  |  |

### NXtranslation

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXtranslation |  |  |  | positions |
| 0/1 | distances |  | NX_FLOAT[numobj,3] |  | positions of components |
| 0/1 |  | units | NX_CHAR | ‘m’ |  |

### NXorientation

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | NXorientation |  |  |  | orientations |
| 0/1 | value |  | NX_FLOAT[numobj,6] |  | orientation information stored as directional cosines |

## Notes:

Coordinate systems: The coordinate system has been revised since Version 1. Coordinate axes are taken with the z-axis pointing along the incident beam direction, the y-axis defined as upwards perpendicular to the beam in the vertical plane and the x-axis perpendicular to the beam in the horizontal plane pointing left as seen from the source. The origin is taken to be at the centre of the spectrometer, usually about the sample position. Cartesian, cylindrical and spherical polar coordinate systems may be used with angles ( (rotation about the z-axis) and θ (rotation about the x-axis), increasing for clockwise rotations viewed from the origin of the coordinate system.

Conventions used in the document: The conventions used in this document are as defined in the paper ‘The ISIS NeXus RAW Data File Format’ by F.A. Akeroyd. In brief, to help understand this document:

- Variables in bold are mandatory, names in italics are examples and any suitable name may be substituted.

- The column headed ‘RE’ indicates how often an item name may occur: 0/1 – optional with a maximum of one instance, 1 – a single instance is mandatory, 0/1+ - not mandatory, but may occur more than once.

- Special variables: np – number of periods, ntc – number of time channels in spectra, ns – number of spectra (histograms), nd – number of detectors and ng – number of groups.

- For strings where the variable should only take certain values, this is indicated by ‘string 1’ | ‘string 2’.

Note 0: The groups ‘NXrunlog’, ‘NXselog’, ‘NXperiod’ and NXdae are defined to store data acquisition parameters and action logs. The intention is to seek ratification of these container classes on the understanding that much of the contents are likely to be facility specific.

Note 1: In line with the latest advice from the NIAC, raw data is now moved to the NXdetector group, i.e. this contains both the parameters describing the detector and the resulting data. The NXdata group contains links to plottable data. Division of data into multiple NXdetector groups may be made according to convenience; strategies might include having an NXdetector group for each physical detector e.g. ‘UP’, ‘DOWN’, etc, or one for each bank of detectors, e.g. the ‘Forward/Backward’ array – the latter strategy is adopted at ISIS. It is suggested that both the NXdetector and NXdata groups are named according to the convention ‘detector_{function}’. The situation where a single physical detector is read using multiple data acquisition electronics should be handled by writing multiple NXdetector groups, where an underscore and instance number is appended to the functional name. For example, for a transverse detector array used to collect data using DAE2 and the DASH2 systems, there would be two NXdetector groups (called ‘detector_transverse_1’ and detector_transverse_2) and two NXdata groups (also called ‘detector_transverse_1’ and ‘detector_transverse_2’).

Note 2: Similar naming schemes exist for defining sample environment (temperature_*) and logged (temperature_*_log) variables, immediately showing the dependence to the variable. Sample environment variables should begin with a prefix that uniquely defines the class of sample environment they describe.

Note 3: Data is collected as a series of spectra (histograms). Usually there is a one to one mapping between the spectra and detectors, but occasionally signals from a number of detectors can be combined to form a single spectrum (muon DAE2 may have this facility in the future), and therefore the number of spectra (ns) can be less than the number of detectors (nd). The proposed detector <-> spectrum indexing scheme is suggested, that follows that proposed for neutron data.

The detectors {i} are numbered i=[1,nd], and their output is mapped onto the spectra {j}. The global spectrum number must be unique, and this number is provided by spectrum_index[j]. The array detector_list contains a list of detector numbers {i}, but they are arranged such that detectors which map to the same spectrum appear sequentially with the start of this sequence given by detector_index[j]. The spectrum spectrum_index[j] will thus have detector_count[j] detectors mapped into it, the actually detector numbers being given by detector_list[k ... k+detector_count[j]-1], where k=detector_index[j].

For a one-to-one mapping between spectra and detectors (usual for µSR experiments), the entries ‘detector_index’, ‘detector_count’ and ‘detector_list’ need not be written.

Note 4: ‘geometry’ (given in group NXgeometry), ‘shape’, ‘size’ and ‘translation’ uniquely define the instrument detector array. These values will usually be ‘engineering’ values, with the calibrated azimuthal angles given in ‘calibrated_angles’.

Note 5: Detector deadtime may be handled in two ways, either by including an array of deadtime values, one for each spectrum, or by an array of coefficients determined from a polynomial fit to the early time distortion; entries are named accordingly.

Note 6: The grouping is represented as a 1D array with the index representing the spectrum number and the value corresponding to the group into which it should be placed. The number and names of groups is defined as an attribute. Multiple groupings for a given detector bank may be written, with the preferred grouping indicated by the ‘primary’ attribute. The grouping entry should only be written if the values can be defined. Possible sources of the grouping information may be a default file or grouping tables derived from analysis programme, e.g. ‘long.uda’ for longitudinal data and ‘trans.uda’ for transverse data from UDA.

Note 7: The balance parameter, alpha, is given for pairs of groups defined in ‘grouping’. Association with a particular grouping entry is by name. Values are stored in a 2D array together with the numbers for the forward and backward groups.

## General comments:

- The NeXus Instrument Definition has entries that define how a wide range of information should be stored in the file. Obviously most entries will be of no use to most people, and therefore their inclusion is optional. Various strategies might be required to automatically capture a comprehensive array of meta-data.

- A number of additional quantities were logged by the MuSR instrument and written to the top level of the Version 1 NeXus file. These entries were not defined by the Instrument Definition; Appendix 2 discusses how these have been incorporated into the Version 2 definition.

- Special experiments (such as RF, illumination, E-field) will require additional entries to fully describe experiment parameters. It is recommended that additional entries are placed into the NeXus file structure as follows:

  - An addendum to the IDF should be defined to show how new entries are written within the muon IDF structure, and clarify their exact meaning. The spirit of the existing IDF should be followed wherever possible when defining new entries.

  - In general, all new entries taken from SECI blocks will be written to the defined NXselog group (see discussion in Appendix 2).

  - New entries should be named using a unique prefix. Where possible conventions suggested by the NIAC should be followed, otherwise e.g. ‘rf_’ for RF experiments, ‘laser_’ for laser experiments, ‘current_’ for currents. A numbered suffix could be used to allow multiple numbers of a specific device. For example, a simple IDF extension for an RF experiment might include ‘rf_frequency’, ‘rf_power’, ‘rf_delay’, ‘rf_pulselength’ and ‘rf_field’, and the definition might be made as follows:

| RE | Name | Attribute | Type | Value | Description |
| --- | --- | --- | --- | --- | --- |
|  | rf_frequency |  | NX_FLOAT32 | rf frquency |  |
|  |  | units | NX_CHAR | ‘MHz’ |  |
|  |  | hardware | NX_CHAR | ‘marconi’ |  |
|  |  | display_name | NX_CHAR | name displayed on DAE software | at ISIS, typically SECI block name |
|  |  | software | NX_CHAR | version of driver used to collect data | at ISIS, typically VI name and version |
|  | rf_delay |  | NX_FLOAT32 | rf delay | relative to extract |
|  |  | units | NX_CHAR | ‘us’ |  |
|  |  | hardware | NX_CHAR | ‘stanford’ |  |
|  |  | display_name | NX_CHAR | name displayed on DAE software | at ISIS, typically SECI block name |
|  |  | software | NX_CHAR | version of driver used to collect data | at ISIS, typically VI name and version |
|  | rf_pulselength |  | NX_FLOAT32 | rf pulse length |  |
|  |  | units | NX_CHAR | ‘us’ |  |
|  |  | hardware | NX_CHAR | ‘CAEN Dual Timer’ |  |
|  |  | display_name | NX_CHAR | name displayed on DAE software | at ISIS, typically SECI block name |
|  |  | software | NX_CHAR | version of driver used to collect data | at ISIS, typically VI name and version |
|  | rf_power |  | NX_FLOAT32 | desired RF power |  |
|  |  | units | NX_CHAR | ‘W’ |  |
|  |  | hardware | NX_CHAR | ‘AMT’ |  |
|  |  | display_name | NX_CHAR | name displayed on DAE software | at ISIS, typically SECI block name |
|  |  | software | NX_CHAR | version of driver used to collect data | at ISIS, typically VI name and version |
|  | rf_power_log |  | NXlog | power log |  |
|  | rf_field |  | NX_FLOAT32 | rf field strength |  |
|  |  | units | NX_CHAR | ‘G’ |  |
|  |  | rf_field_vector | NX_FLOAT[3] | vector describing orientation of RF field |  |
|  |  | display_name | NX_CHAR | name displayed on DAE software | at ISIS, typically SECI block name |
|  |  | software | NX_CHAR | version of driver used to collect data | at ISIS, typically VI name and version |

## Appendix 1: Class definitions unique to ‘muonTD’

The following class names are used in the definition of ‘muonTD’ that have not previously been defined and ratified by the NIAC. The intention is to seek ratification in order that classes and certain entry names can be reserved for muon applications.

- NXrunlog:
A container for time logged parameters relating to the run.

- NXselog:
A container for time logger parameters relating to the sample environment.

- NXperiod:
A container for parameters relating to operation of period data acquisition.

- NXdae:
A container for information about the data acquisition electronics.

- NXbeamline:
Information on the beamline between target and instrument, and therefore an entry of NXinstrument.

- NXdiagnostics:
A container for diagnostic information on beamline function (for inclusion in NXbeamline).

- NXdipole_magnet:
(aka dipole) defined by the NIAC as NXbending_magnet, but change of name is requested and definition requires extension (for inclusion in NXbeamline).

- NXquadrupole_magnet:
Class definition for a quadrupole magnet (for inclusion in NXbeamline).

- NXsolenoid_magnet:
Class definition for a solenoid magnet (for inclusion in NXbeamline).

- NXmagnetic_kicker:
Class definition for a magnetic beam kicker (for inclusion in NXbeamline).

- NXelectrostatic_kicker:
Class definition for a magnetic beam kicker (for inclusion in NXbeamline).

- NXseparator:
Class definition for a particle separator (for inclusion in NXbeamline).

- NXspin_rotator:
Class definition for a spin rotator (for inclusion in NXbeamline).

- NXseptum_magnet:
Class definition for a septum magnet (for inclusion in NXbeamline).

- NXbeamline_collimator:
Class definition for a beamline collimator (for inclusion in NXbeamline).

- NXuif
Container class for additional data/information defined by the user.

In addition, the intention is to ratify the name ‘idf_version’ (for inclusion in NXentry) as a means of the muon community identifying the version of the Instrument Definition File (IDF) that the data file conforms to. It should be noted, that the recent muon data files are written containing both ‘idf_version’ and ‘IDF_version’, and therefore interrogating either case will yield a definite result.

The muon community would also value an extension to the definition of NXlog to enable information stored as a one dimensional array to be logged as a function of time. This facility is important for allowing vector fields to be stored (see entry for the magnetic field log in NXsample) and enabling, for example, traces recorded from oscilloscopes to be preserved.

## Appendix 2: Incorporating SECI logged values

The ISIS Instrument Control Program (ICP), and particularly the Sample Environment Control Interface (SECI), enables the user to define logged parameters through the use of ‘blocks’. Since SECI allows the user to load additional LabView VIs and associate ‘blocks’ with LabView values, the number of values logged by SECI may be almost unlimited. Clearly it is desirable for any value logged by SECI to be available in the data file, and indeed it is the current practice at ISIS to write all SECI defined ‘blocks’ when the run is completed.

Given the unlimited nature of the information that may be recorded by SECI, it is quite possible that ‘blocks’ may be defined that contain information that is beyond the scope of the Instrument Definition. Therefore, the following strategy has been adopted at ISIS for writing this information: a) all logged values associated with all SECI ‘blocks’ are written to a container group ‘NXselog’; b) logged values defined throughout the Instrument Definition are actually formed by links pointing to the relevant information within the NXselog group.

It should be noted that if parameters are regularly stored outside the scope of the Instrument Definition, consideration should be given to defining extensions to the Definition (e.g. an extended description for inclusion within NXsample).

# Text boxes

Beam direction

z

x

y

θ

φ